## Slide 1: Trusted Execution Environments
Chester Rebeiro
IIT Madras
Some of the slides borrowed from Intel; CDACH; ARM

## Slide 2: Previously in SSE…
We looked at techniques to run an untrusted code safely
Run Program Here
If misbehaves
Kill it
System
Confinement

## Slide 3: Today in SSE…
We now look at how to run sensitive code in an untrusted environment
  Besides other applications, the OS can also be untrusted.
  Attackers can probe hardware
What to worry about:
  Code / Data of the sensitive app gets read / modified by the system
Run Sensitive
Program Here
Untrusted System
Trusted Execution Environment

## Slide 4: Basic Problem (Ring Architecture)

## Slide 5: Basic Problem (Ring Architecture)

## Slide 6: Invasive Attacks

## Slide 7: Trusted Execution Environments
Achieve confidentiality and integrity even when the OS is compromised!
ARM : Trustzone (trusted execution environments)
Intel : SGX (enclaves)

## Slide 8: ARM Trustzone
Trustzone Security Whitepaper, ARM
http://infocenter.arm.com/help/topic/com.arm.doc.prd29-genc-009492c/PRD29GENC-009492C_trustzone_security_whitepaper.pdf
Some of the slides borrowed from CDACH; ARM

## Slide 9: ARM System on Chips

## Slide 10: ARM Trustzone (Main Idea)
Hardware and Software partitioned into two: Normal and Secure worlds
A single hardware processor timesliced between secure and normal worlds
Secure world provides an environment that supports confidentiality and integrity.
Can prevent software attacks
Cannot prevent invasive attacks

## Slide 11: A Typical Trustzone Application

## Slide 12: Switching Worlds
Execution in time sliced manner (Secure <-> Normal)
New mode (monitor mode) that is invoked during switching modes
Mode switching
  triggered by secure monitoring call (SMC) instruction
  certain hardware exceptions (interrupts, aborts)
Monitor Mode: saves state of the current world and restores the state of the world being switched to. Restoration by return-from-exception.
NS Bit: in configuration register indicates secure / normal operating mode.
NS = 1 -> indicates non-secure (normal) mode

## Slide 13: NS Bit extends beyond the chip

## Slide 14: NS Bit extends beyond the chip

## Slide 15: Memory Management
CPU Core
Memory (RAM)
VA NSTID
MMU
page tables
page tables
Physical address
Physical address
Non Secure Table Identifier
current state of the processor (0 if secure world / 1 if normal
world
If NSTID = 1 then force NS bit to 1
Virtual address (VA) have an extra bit (33-rd bit) to
Notes: Non Secure Table Identifier --- current state of the processor

## Slide 16: Memory Management
CPU Core
Memory (RAM)
VA NSTID
VA NSTID
PA NS
MMU
page tables
page tables
Physical address
Physical address
VA NSTID
PA NS
VA NSTID
PA NS
VA NSTID
PA NS
TLB
Page walk only
on TLB miss
TLB stores NSTID and NS bit per entry
Notes: Non Secure Table Identifier --- current state of the processor

## Slide 17: Memory Management
CPU Core
Memory (RAM)
VA NSTID
VA NSTID
PA NS
MMU
page tables
page tables
Physical address
Physical address
VA NSTID
PA NS
VA NSTID
PA NS
VA NSTID
PA NS
TLB
Page walk only
on TLB miss
Secure world page tables can map to normal world memory
Notes: Non Secure Table Identifier --- current state of the processor

## Slide 18: Memory Management
CPU Core
Memory (RAM)
VA NSTID
VA NSTID
PA NS
MMU
page tables
page tables
Access RAM only on cache miss
VA NSTID
PA NS
VA NSTID
PA NS
VA NSTID
PA NS
TLB
Page walk only
on TLB miss
Tag NS
cache line
Tag NS
cache line
Tag NS
cache line
Tag NS
cache line
Cache Memory
PA
Notes: Non Secure Table Identifier --- current state of the processor

## Slide 19: Memory Management Units
Two virtual MMUs (one for each mode)
  Two page-tables active simultaneously
A single TLB present
  A tag in each TLB entry determines the mode (Normal and Secure TLB entries may co-exist; this allows for quicker switching of modes)
  alternatively the monitor may flush the TLB whenever switching mode
A single cache is present
  Tags (again) in each line used to store state
  Any non-locked down cache line can be evicted to make space for new data
  A secure line load can evict a non-secure line load (and vice-versa)

## Slide 20: Secure and Normal Devices

## Slide 21: Interrupts
All interrupts routed to monitor first.
Interrupts can be configured to go either to the normal world or secure world.
User Code
Privileged Code
User Code
Privileged Code
Monitor
IRQ
IRQ
Normal world
Secure world
IRQ

## Slide 22: Interrupts
All interrupts routed to monitor first.
Interrupts can be configured to go either to the normal world or secure world.
User Code
Privileged Code
User Code
Privileged Code
Monitor
IRQ
IRQ
Normal World Interrupt Vector Table
Monitor Interrupt Vector Table
Secure World
Interrupt Vector Table
Normal world
Secure world

## Slide 23: Software Architecture
The minimal secure world can just have implementations of synchronous code libraries
Typically has an entire operating system
  Qualcomm’s QSEE; Trustonics Kinibi; Samsung Knox; Genode
  The secure OS could be tightly couples to the rich OS so that a priority of a task in the rich OS gets mapped accordingly in the secure OS
  Advantage of having a full OS is that we will have complete MMU support
Intermediate Options

## Slide 24: Secure Boot
Why?
Attackers may replace the flash software with a malicious version, compromising
the entire system.
How?
Secure chain of trust.
Starting from a root device (root of trust) that cannot be easily tampered

## Slide 25: Secure Boot Sequence

## Slide 26: Chain of Trust
Inherently secure
Component
(PUF/ TPM/ onchipROM)
Root of trust
Boot loader
check signature
Secure OS
check signature
Rich OS
check signature
Trustlet
Trustlet
Trustlet
check signature
check signature
check signature
Notes: Onchip ROM 

## Slide 27: Points to Ponder
Describe how ARM trustzone can handle invasive attacks?
What can it handle?
What are the limitations?