## Slide 1: Micro-architectural Attacks
Chester Rebeiro
IIT Madras

## Slide 2: Things we thought gave us security!
Cryptography
Passwords
Information Flow Policies
Privileged Rings
ASLR
Virtual Machines and confinement
Javascript and HTML5 (due to restricted access to system resouces)
Enclaves (SGX and Trustzone)

## Slide 3: Micro-Architectural Attacks (can break all of this)
Cache timing attack
Branch prediction attack
Speculation Attacks
Row hammer
Fault Injection Attacks
….. and many more
cold boot attacks
Cryptography
Passwords
Information Flow Policies
Privileged Rings
ASLR
Virtual Machines and confinement
Javascript and HTML5 (due to restricted access to system resouces)
Enclaves (SGX and Trustzone)
DRAM Row buffer (DRAMA)

## Slide 4: Causes
performance
security
Most micro-architectural attacks caused by performance optimizations
Others due to inherent device properties
Third, due to stronger attackers

## Slide 5: Cache Covert Channel
Chester Rebeiro
Indian Institute of Technology Madras

## Slide 6: Cache Covert Channel
Processes
Processor
Memory
Cache
Memory

## Slide 7: Cache Covert Channel
cache line
cache set
way
Processes
Processor
Memory
Cache
Memory

## Slide 8: Cache Covert Channel
cache line
tag
address
set
line
chooses one set

## Slide 9: Cache Covert Channel
Process P2
while(1){
load A1p2; load A2p2
load A3p2; load A4p2
load B1p2; load B2p2
load B3p2; load B4p2
}
A Set
B Set
statistically
time A ~ time B

## Slide 10: Cache Covert Channel
Process P1
Process P2
A Set
B Set
If (bit == 1) load AP1
Else
load BP1
statistically
time A > time B
while(1){
load A1p2; load A2p2
load A3p2; load A4p2
load B1p2; load B2p2
load B3p2; load B4p2
}

## Slide 11: Cache Covert Channel
Process P1
Process P2
A Set
B Set
If (bit == 1) load AP1
Else
load BP1
statistically
time A < time B
while(1){
load A1p2; load A2p2
load A3p2; load A4p2
load B1p2; load B2p2
load B3p2; load B4p2
}

## Slide 12: Cache Covert Channel
Process P1
Process P2
while(1){
load A1p2; load A2p2
load A3p2; load A4p2
load B1p2; load B2p2
load B3p2; load B4p2
}
bit = message
while(bit[i] != ‘\0’)
for(some number of iterations)
If (bit[i] == 1) load AP1
else
load BP1
statistically
time A < time B

## Slide 13: Covert Channels
Identifying: Not easy because simple things like the existence of a file, time, etc. could be a source for a covert channel.
Quantification: communication rate (bps)
Elimination: Careful design, separation, characteristics of operation (eg. rate of opening / closing a file)

## Slide 14: Flush+Reload Attacks
Chester Rebeiro
IIT Madras

## Slide 15: Copy on Write
if (fork() > 0){
// in parent process
} else{
// in child process
}
Child created is an exact replica of the parent process.
Page tables of the parent duplicated in the child
New pages created only when parent (or child) modifies data
  Postpone copying of pages as much as possible, thus optimizing performance
  Thus, common code sections (like libraries) would be shared across processes.

## Slide 16: Process Tree
:
SSLEncryption()
:
init
:
SSLEncryption()
:
Physical Memory
Virtual Memory
(process 1)
Virtual Memory
(process 2)

## Slide 17: Interaction with the LLC
Processes
Core 1
LLC
:
SSLEncryption()
:
cache misses
slow
Core 2
Processes

## Slide 18: Interaction with the LLC
:
SSLEncryption()
:
cache hits
:
SSLEncryption()
:
fast
One process can affect the execution time of another process
Processes
Core 1
LLC
Core 2
Processes

## Slide 19: Flush + Reload Attack on LLC
Part of an encryption algorithm
executed only when ei = 1
clflush Instruction
Takes an address as input.
Flushes that address from all caches
clflush (line 8)
Flush+Reload Attack, Yuval Yarom and Katrina Falkner (https://eprint.iacr.org/2013/448.pdf)

## Slide 20: Flush + Reload Attack
:
SSLEncryption()
:
:
Clflush(line 8)
:
flush
reload
access
victim
attacker
Processes
Core 1
LLC
Core 2
Processes

## Slide 21: Flush+Reload Attack

## Slide 22: Countermeasures
Do not use copy-on-write
  Implemented by cloud providers
Permission checks for clflush
  Do we need clflush?
Non-inclusive cache memories
  AMD
  Intel i9 versions
Fuzzing Clocks
Software Diversification
  Permute location of objects in memory (statically and dynamically)

## Slide 23: Cache Collision Attacks
Chester Rebeiro
IIT Madras

## Slide 24: Cache Collision Attacks
External Collision Attacks
  Prime + Probe
Internal Collision Attacks
  Time-driven attacks

## Slide 25: Prime + Probe Attack
Core 1
Last Level Cache
Core 2
Victim
SMT Core
L1 Cache Memory
Spy
Victim
Spy
way 0
way 1
way 2
way 3
Set 0
Set 1
Set 2
Set 3
Set N-2
Set N-1

## Slide 26: Prime Phase
way 0
way 1
way 2
way 3
Set 0
Set 1
Set 2
Set 3
While(1){
for(each cache set){
start = time();
access all cache ways
end = time();
access_time = end – start
}
wait for some time
}

## Slide 27: Victim Execution
way 0
way 1
way 2
way 3
Set 0
Set 1
Set 2
Set 3
The execution causes some of the spy data to get evicted

## Slide 28: Probe Phase
way 0
way 1
way 2
way 3
Set 0
Set 1
Set 2
Set 3
While(1){
for(each cache set){
start = time();
access all cache ways
end = time();
access_time = end – start
}
wait for some time
}
Time taken by sets that have victim data is more due to the cache misses

## Slide 29: Probe Time Plot
0
63
Each row is an iteration of the while loop; darker shades imply higher memory access time

## Slide 30: Prime + Probe in Cryptography
char Lookup[] = {x, x, x, . . . x};
char RecvDecrypt(socket){
char key = 0x12;
char pt, ct;
read(socket, &ct, 1);
pt = Lookup[key ^ ct];
return pt;
}
The attacker know the address of Lookup and the ciphertext (ct)
The memory accessed in Lookup depends on the value of key
Given the set number, one can identify bits of key ^ ct.
Key dependent memory accesses

## Slide 31: Keystroke Sniffing
Keystroke  interrupt  kernel mode switch  ISR execution  add to keyboard buffer  …  return from interrupt
way 0
way 1
way 2
way 3
Set 0
Set 1
Set 2
Set 3

## Slide 32: Keystroke Sniffing
Regular disturbance seen in Probe Time Plot
Period between disturbance used to predict passwords
Svetlana Pinet, Johannes C. Ziegler, and F.-Xavier Alario. 2016. Typing Is Writing: Linguistic Properties Modulate Typing Execution. Psychon Bull Rev 23, 6

## Slide 33: Web Browser Attacks
Prime+Probe in
  Javascript
  pNACL
  Web assembly

## Slide 34: Extract Gmail secret key
https://www.cs.tau.ac.il/~tromer/drivebycache/drivebycache.pdf

## Slide 35: Website Fingerprinting
Privacy: Find out what websites are being browsed.

## Slide 36: Cross VM Attacks (Cache)

## Slide 37: Cross VM Attacks (DRAM)

## Slide 38: Internal Collision Attacks
(Adversary)
Victim

## Slide 39: Internal Collisions on a Cipher
Table
Table
Part of a Cipher
P0
,P4
(Adversary)
39
  If cache hit (less time) :
  If cache miss (more time):

## Slide 40
T
P0
K0
T
P4
K4
Block Cipher
Random
P0
Cipher Text
P4
  Suppose
  (K0 = 00 and k4 = 50)
P0 = 0, all other inputs are random
Make N time measurements
Segregate into Y buckets based on value of P4
Find average time of each bucket
Find deviation of each average from overall average (DOM)
P4 | Average Time | DOM
00 | 2945.3 | 1.8
10 | 2944.4 | 0.9
20 | 2943.7 | 0.2
30 | 2943.7 | 0.2
40 | 2944.8 | 1.3
50 | 2937.4 | -6.3
60 | 2943.3 | -0.2
70 | 2945.8 | 2.3
: | : | :
F0 | 2941.8 | -1.7
Average : 2943.57
Maximum : -6.3

## Slide 41
Implementation | Difference of Means
AES (OpenSSL 0.9.8a ) | -6.5
DES (PolarSSL 1.1.1 ) | +11
CAMELLIA (PolarSSL 1.1.1) | 19.2
CLEFIA (Ref. Implementation 1.0) | 23.4
Easiness to attack

## Slide 42: Speculation Attacks
Some of the slides motivated from Yuval Yarom’s talk on Meltdown and Spectre at the Cyber security research bootcamp 2018

## Slide 43: Out-of-order execution
load r0, addr1
mov r2, r1
add r2, r2, r3
store r1, add2
sub r4, r5, r6
How instructions are
fetched
sub r4, r5, r6
store r1, add2
mov r2, r1
add r2, r2, r3
load r0, addr1
How they may be
executed
r0
r2
r2
addr2
r4
How the results are
committed
inorder
order restored
out-of-order
Out the processor core, execution looks in-order
Insider the processor core, execution is done out-of-order

## Slide 44: Speculative Execution
cmp r0, r1
jnz label
load r0, addr1
mov r2, r1
add r2, r2, r3
store r1, add2
sub r4, r5, r6
:
:
:
label:
more instructions
cmp r0, r1
jnz label
load r0, addr1
mov r2, r1
add r2, r2, r3
store r1, add2
sub r4, r5, r6
:
:
:
label:
more instructions
How instructions are
fetched
How instructions are
executed
r0
r2
r2
add2
r4
:
:
:
How results are committed when speculation is correct
Speculative execution
(transient instructions)

## Slide 45: Speculative Execution
cmp r0, r1
jnz label
load r0, addr1
mov r2, r1
add r2, r2, r3
store r1, add2
sub r4, r5, r6
:
:
:
label:
more instructions
cmp r0, r1
jnz label
load r0, addr1
mov r2, r1
add r2, r2, r3
store r1, add2
sub r4, r5, r6
:
:
:
label:
more instructions
How instructions are
fetched
How instructions are
executed
:
:
:
How results are committed when speculation is incorrect
Speculative execution
(transient instructions)
Speculated results
discarded

## Slide 46: Speculative Execution
cmp r0, r1
div r0, r1
load r0, addr1
mov r2, r1
add r2, r2, r3
store r1, add2
sub r4, r5, r6
:
:
:
label:
more instructions
cmp r0, r1
div r0, r1
load r0, addr1
mov r2, r1
add r2, r2, r3
store r1, add2
sub r4, r5, r6
:
:
:
label:
more instructions
How instructions are
fetched
How instructions are
executed
:
:
:
How results are committed when speculation is incorrect
(eg. If r1 = 0)
Speculative execution
Speculated results
discarded

## Slide 47: Speculative Execution and Micro-architectural State
Even though line 3 is not reached, the micro-architectural state is modified due
to Line 3.
data=84

## Slide 48: Meltdown
User space
Kernel space
Virtual address space of process
i = *pointer y = array[i * 256]
*pointer
array
way 0
way 1
way 2
way 3
Set 0
Set 1
Set 2
Set 3
Cache Memory
Normal Circumstances

## Slide 49: Meltdown
User space
Kernel space
Virtual address space of process
i = *pointer y = array[i * 256]
*pointer
array
way 0
way 1
way 2
way 3
Set 0
Set 1
Set 2
Set 3
Cache Memory
Not normal Circumstances

## Slide 50: Meltdown
User space
Kernel space
Virtual address space of process
i = *pointer y = array[i * 256]
*pointer
array
way 0
way 1
way 2
way 3
Set 0
Set 1
Set 2
Set 3
Cache Memory
Not normal Circumstances
cache miss

## Slide 51: Meltdown
User space
Kernel space
Virtual address space of process
i = *pointer y = array[i * 256]
*pointer
array
way 0
way 1
way 2
way 3
Set 0
Set 1
Set 2
Set 3
Cache Memory
Not normal Circumstances
cache miss

## Slide 52: Meltdown
User space
Kernel space
Virtual address space of process
i = *pointer y = array[i * 256]
*pointer
array
way 0
way 1
way 2
way 3
Set 0
Set 1
Set 2
Set 3
Cache Memory
Not normal Circumstances
cache miss

## Slide 53: Meltdown
User space
Kernel space
Virtual address space of process
i = *pointer y = array[i * 256]
*pointer
array
way 0
way 1
way 2
way 3
Set 0
Set 1
Set 2
Set 3
Cache Memory
Not normal Circumstances
cache hit

## Slide 54: Spectre
Slides motivated from Yuval Yarom’s talk on Meltdown and Spectre at the Cyber security research bootcamp 2018

## Slide 55: Spectre (variant 1)
if (x < array_len){
i = array[x];
y = array2[i * 256];
}
user space of a process
array2
x
array
secret
array_len
Cache memory

## Slide 56: Spectre (variant 1)
if (x < array_len){
i = array[x];
y = array2[i * 256];
}
user space of a process
array2
x
array
secret
array_len
Cache memory
<

## Slide 57: Spectre (variant 1)
if (x < array_len){
i = array[x];
y = array2[i * 256];
}
user space of a process
array2
x
array
secret
array_len
Cache memory
Normal Behavior

## Slide 58: Spectre (variant 1)
if (x < array_len){
i = array[x];
y = array2[i * 256];
}
user space of a process
array2
x
array
secret
array_len
Cache memory
x 256
Normal Behavior

## Slide 59: Spectre (variant 1)
if (x < array_len){
i = array[x];
y = array2[i * 256];
}
user space of a process
array2
x
array
secret
array_len
Cache memory
x 256
Normal Behavior

## Slide 60: Spectre (variant 1)
if (x < array_len){
i = array[x];
y = array2[i * 256];
}
user space of a process
array2
x
array
secret
array_len
Cache memory
x 256
Normal Behavior

## Slide 61: Spectre (variant 1)
if (x < array_len){
i = array[x];
y = array2[i * 256];
}
user space of a process
array2
x
array
secret
array_len
Cache memory
Under Attack
x > array_len
array_len not in cache
secret in cache memory

## Slide 62: Spectre (variant 1)
if (x < array_len){
i = array[x];
y = array2[i * 256];
}
user space of a process
array2
x
array
secret
array_len
Misprediction!
<

## Slide 63: Spectre (variant 1)
if (x < array_len){
i = array[x];
y = array2[i * 256];
}
user space of a process
array2
x
array
secret
array_len
Misprediction!
<

## Slide 64: Spectre (variant 1)
if (x < array_len){
i = array[x];
y = array2[i * 256];
}
user space of a process
array2
x
array
secret
array_len
Cache hit found only here

## Slide 65: Spectre (variant 2)
Victim’s
address space
Attacker’s
address space
Some gadget
Jmp *ebx
Jmp *eax
ret

## Slide 66: Spectre (variant 2)
Victim’s
address space
Attacker’s
address space
Some gadget
Jmp *eax
ret
Jmp *ebx
context
switch

## Slide 67: Countermeasures
For meltdown: kpti (kernel page table isolation)

## Slide 68: Countermeasures
For Spectre (variant 1): compiler patches
use barriers (LFENCE instruction) to prevent speculation
static analysis to identify locations where attackers can control
speculation

## Slide 69: Countermeasures
For Spectre (Variant 2): Separate BTBs for each process
  Prevent BTBs across SMT threads
  Prevent user code does not learn from lower security execution

## Slide 70: Countermeasures
For all: at hardware
  Every speculative load and store should bypass cache and stored in a special buffer known as speculative buffer